## Slide 1
Near the earthquake, there were only ~20 minutes to evacuate. A “local tsunami” for Japan.
Travel times are well known for tsunamis crossing the Pacific Ocean.
At distant locations, there were hours of advance warning. A “distant tsunami” for Oregon coast.
Pacific Ocean Tsunami Generated by Japan Earthquake

## Slide 2
Pacific Ocean Tsunami Generated by Japan Earthquake
Tsunami height model shows forecast wave height (in cm).
Ocean floor bathymetry affects the wave height because of reflections and refractions from seafloor features and islands.
Tsunami evacuations were ordered for Hawaii, Oregon, and northern California but not Washington. Wave heights were accurately predicted.

## Slide 3: Deep-ocean Assessment and Reporting of Tsunami (DART)

## Slide 4
Peak-to-trough wave height was nearly 2 m at nearest DART buoy in 4000 m water depth!
Travel time to Oregon and Washington coast was about 9 hours.
Largest waves affected OR and CA MANY hours after first waves arrived.
Pacific Ocean Tsunami Generated by Japan Earthquake

## Slide 5
About four hours travel time to Oregon Coast.
Tsunami from 1964 Alaska EQ killed 4 children on Beverly Beach. The largest of 28 distant tsunamis to affect Oregon coast since 1854.
Significant damage in Seaside and Cannon Beach. Major destruction and 13 deaths in Crescent City, CA.
Pacific Ocean Tsunami Generated by Alaska Earthquake

## Slide 6
Bridge over Elk Creek (now Ecola Creek) destroyed and displaced 300 m upstream.
House torn from foundation and displaced 400 m upstream.
Damage in Cannon Beach from 1964 Alaska Tsunami
From Priest and others, DOGAMI Special Paper 41, 2009.

## Slide 7: Distant Tsunami Inundation Map for Bandon, Oregon

## Slide 8: Past Great Cascadia Earthquakes and Tsunamis
Juan de Fuca subducts beneath Pacific Northwest portion of North American Plate at Cascadia subduction zone.
Last great Cascadia earthquake occurred on January 26, 1700 at about 9:00 PM local time.
Analogous to Sumatra 2004, Chile 2010, and Tohoku, Japan 2011 great earthquakes.

## Slide 9: Yuriage
Some Coast Areas Now Below Sea Level
Before After
Some areas that were above sea level on march 10 dropped below sea level on March 11, 2011.
This also happened along the Washington - Oregon coast during the 1700 AD great Cascadia earthquake.

## Slide 10: Drowned Forests of Coastal Oregon and Washington
Coastal “drowned forests” record the history of slow uplift between and sudden subsidence during great Cascadia earthquakes.
Ghost forest on Copalis River
Brian Atwater, USGS Seattle

## Slide 11: Drowned Forests of Coastal Oregon and Washington
Trees in “drowned forests” near shore died when the ground dropped and seawater killed the trees. Compare rings from victim trees with rings from witness trees on higher ground.
Result: Trees died between fall 1699 and spring 1700.
David Yamaguchi

## Slide 12: Three-Layer Cake of Cascadia Tsunami Geology
Organic-rich forest soil covered by tsunami sand then intertidal mud and clay on top.
Niawiakum River east of Willapa Bay
Cupcake Geology

## Slide 13
inland
Clump of marsh grass
Multiple sand layers.
One for each wave of the tsunami!
Cascadia Tsunami Geology

## Slide 14
Making a Ghost Forest
Notes: Show Formation of Ghost Forest animation of discovery of the 1700 AD great Cascadia earthquake as illustration of scientific discovery.

## Slide 15
Niawiakum River, east of Willapa Bay, WA.
Buried Forest Soils
1700 AD
860(?) AD
Notes: This photo shows roots Sitka spruce trees that were killed by ground subsidence during the 1700 AD great Cascadia earthquake AND the preceding great Cascadia earthquake. This field site is located on the Niawiakum River just east of Willapa Bay in southwestern Washington state.
VIRTUAL FIELD EXPERIENCE: A virtual field experience for this field site is provided on this DVD at: 6.TOTLE VFE and Field Trips > Virtual Field Experiences
To run the virtual field experience from this DVD, open the “index.html” file in the Virtual Field Experiences folder in a web browser such as Safari or Firefox or Explorer.

## Slide 16
Average time between earthquakes = Recurrence time.
Recurrence time for Great Cascadia EQs = 500 years.
We are at 315 years and counting.
Recent Great Cascadia Earthquakes
Notes: From At Risk: Earthquakes and Tsunamis on the West Coast, by J. Clague and others.

## Slide 17
Cascadia Tsunami Geology Storyline
Great earthquake January 26, 1700 @ 9 PM
Ghost forests, buried soils, diatoms, tsunami sand sheets, liquefaction, turbidites, Native American oral history, and written Japanese history.
Intertidal mud & clay
Tsunami sand
Forest soil

## Slide 18
Sediment deposited on continental shelf can surge down submarine canyons in turbidity currents. The resulting “turbidite” layer has coarse sand on bottom and fine clay on top.
Turbidites in Marine Sediment Cores
Turbidite in a Jar

## Slide 19
Chris Goldfinger (OSU).
Shaking by great Cascadia earthquakes caused turbidity currents.
Ages of many seafloor turbidites match from offshore northern CA to BC.
Requires great earthquakes that ruptured entire or large segments of the plate boundary.
Turbidites in Marine Sediment Cores

## Slide 20: Turbidites: The Movie

## Slide 21
Plate Boundary Observatory (PBO)
-1100 permanent Global Positioning System (GPS) stations
-78 Borehole Seismometers
-74 Borehole Strainmeters (BSM)
-26 Tiltmeters
-6 Laser Strainmeters (LSM)
Measure the broad temporal and spatial spectrum of plate boundary deformation

## Slide 22
Cascadia Locked and Loading
Examine motions of GPS stations due to Juan de Fuca - North America plate convergence.
Astoria
Juan de Fuca Plate

## Slide 23
Northward motion = 0.29 inch/yr
Eastward motion = 0.33 inch/yr
Astoria, OR GPS Observations
Total motion = 0.44 inch/yr
Total motion since 1700 AD = 11.5 feet

## Slide 24: Cascadia GPS Animation

## Slide 25
Stations on coast are moving NE faster than stations in urban corridor.
Cascadia subduction zone boundary is “locked and loading” as it stores elastic energy that will be released in the next great Cascadia earthquake.
If the next great Cascadia earthquake happens tomorrow, Pacific Beach will jump 5.35 meters (17.5 feet) southwest.
Corvallis
Pacific
Beach
Neah
Bay
Kelso
Tumwater
Othello
La Grande
Wasco
Tillamook
Newport
Cascadia Locked and Loading
Juan de Fuca Plate
GPS Gum Drop

## Slide 26
Neah Bay, WA GPS Data
42 mm / 5.5 yr = 7.6 mm/yr
56mm / 5.5 yr = 10.2 mm/yr
2006
2007
2008
2004
2005
2009

## Slide 27
Neah Bay, WA GPS Velocity
12.4 mm / yr

## Slide 28
GPS receivers in western part of the Willamette Valley and Puget Lowlands, as well as the eastern fringe of the Coast Ranges, move in a “sawtooth pattern”.
They move NE most of the time but backslide to the SW every 10 to 16 months.
Low-amplitude seismic vibrations accompany the backwards motion.
This is “Episodic Tremor and Slip”, a major new discovery.
Corvallis
Pacific
Beach
Neah
Bay
Kelso
Tumwater
Othello
La Grande
Wasco
Tillamook
Newport
Juan de Fuca Plate
Episodic Tremor and Slip

## Slide 29
Animation by JENDA JOHNSON
Episodic Tremor and Slip

## Slide 30
Slow slip between North American and Juan de Fuca plates at 20 – 40 km depth. A transitional behavior between the shallow locked zone and the continuously slipping zone deeper than 40 km.
Episodic Tremor and Slip
Two-Block EQ Model

## Slide 31
Episodic Tremor and Slip
Animation by JENDA JOHNSON

## Slide 32: PNW Crustal Block Motions
Crustal blocks are in slow motion. They grind against each other causing EQs along their edges. They also deform internally to make faults and folds.
PNW Crustal Block Model

## Slide 33: Animation on Crustal Block Motions

## Slide 34: PNW Crustal Block Motions
Explore the model.
Note rotation of Coast Range blocks and opening of Basin and Range in southeastern Oregon.
PNW Crustal Block Model

## Slide 35: Crustal Earthquakes in Oregon 1841 - 2002
Klamath Falls, 1993
Mt Angel, 1993

## Slide 36: Cascadia Earthquake Early Warning

## Slide 37: Local Cascadia Tsunami
DOGAMI has published Tsunami Inundation Maps based on modeling of tsunamis generated by great earthquakes on the Cascadia subduction zone.
Important factors:
Western edge of North American plate.
Displacement during great earthquakes: How much? How deep? A splay fault?
Bathymetry of ocean floor on continental slope and shelf.
Shoreline topography.
Note that WA continental shelf is wider than OR continental shelf.

## Slide 38
Continental Shelf Deformation? Splay Faults?

## Slide 39: Local Tsunami Inundation Map for Bandon
SM = “small” M8.8 Cascadia EQ of 9 m displacement (300 years of plate motion).
M = “medium” M8.9 Cascadia EQ of 15 m displacement (500 years of plate motion).
L = “large” M9.0 Cascadia EQ of 23 m displacement (750 years of plate motion).
XL = “extra-large” M9.1 Cascadia EQ of 35 m displacement (1100 years of plate motion).
XXL = “extra-extra-large” M9.2 Cascadia EQ of 40 m displacement (1200 years of plate motion).
Numbers refer to rupture model.
Tsunami Inundation Maps

## Slide 40: Tsunami Evacuation Map for Bandon, Oregon
Distant tsunami evacuation zone determined from maximum Alaska tsunami.
Local Tsunami Evacuation Zone determined from maximum Cascadia tsunami.
Wave-Tank Tsunami Model

## Slide 41
Ocosta Elementary School
If you can’t get out, go up.

## Slide 42: NOAA Video on Vertical Evacuation from Tsunamis
Notes: URL = http://www.fema.gov/medialibrary/media_records/8086

## Slide 43: IRIS Home Page
Educational Resources
Notes: IRIS Home Page: http://www.iris.edu/hq/

## Slide 44: IRIS “Educational Resources” Page
Animations
Notes: IRIS Educational Resources Page: http://www.iris.edu/hq/programs/education_and_outreach
IRIS Animations Page: http://www.iris.edu/hq/programs/education_and_outreach/animations

## Slide 45: IRIS Home Page
Recent Earthquake
Teachable Moments
Notes: IRIS Recent Earthquakes Teachable Moments Page: http://www.iris.edu/hq/retm

## Slide 46
IRIS Recent Earthquake Teachable Moments
Notices developed for all M > 7 earthquakes worldwide.
336,000 views Jan 1 – March 19, 2011.
Sign up for the listserv to receive email notice when new RETMs are posted.
Notes: Japan March 11, 2011 Recent Earthquake Teachable Moment: http://www.iris.edu/hq/retm/event/1328

## Slide 47: Tsunami Evacuation Map for Bandon, Oregon
Distant tsunami evacuation zone determined from maximum Alaska tsunami.
Local Tsunami Evacuation Zone determined from maximum Cascadia tsunami.

## Slide 48: Cascadia Earthquake Displacement Models
Example for a “medium” size (M8.9) Cascadia earthquake (500-year recurrence time and 15 m offset).
M1: Shallow displacement occurs on splay fault.
M2: Displacement to deformation front.
M3: Displacement stops a few km below the seafloor.

## Slide 49: Cascadia Earthquake Vertical-Offset Models
Example for a “medium” size (M8.9) Cascadia earthquake.
M1: Produces 5 m uplift of seafloor offshore from Newport.
M2: Produces 4 m uplift of seafloor offshore from Newport.
M3: Produces 4 m uplift of seafloor offshore from Newport.
Note the change in shape of uplifted seafloor area.

## Slide 50: Measured GPS Velocities
What’s up with southwestern Oregon?
Shouldn’t ALL the velocities vectors on PNW coast be parallel to Juan de Fuca motion as it converges with North America?

## Slide 51
Juan de Fuca – North America convergence ALONE should produce simple pattern of velocities like this.
Compression of Pacific Northwest Continental Margin

## Slide 52
Crustal Block Motions + Plate Convergent Motions
Convergence
velocities in red.
Crustal block
Motion velocities in orange.
Observed GPS velocities.
+
=